## Slide 1: Hardware Development with NFC
张庭梁
Future Laboratory, Academy of Art and Design
Tsinghua University

## Slide 2: About Me
本科电机系，跑路到美院信息艺术设计交叉学科，目前研一
一直在搞乱七八糟的硬件开发，啥好玩就搞什么
曾任清华大学“未来通信”学生科技兴趣团队理事长， “天空工场”学生科技兴趣团队“未来航空队”队长
去年挑战杯特奖（狗头

## Slide 3: Preview of iTag

## Slide 10: Quiz
导体和绝缘体区分
电路串并联
电路板是什么
在面包板上搭过电路
画过电路板
做过完整的硬件工程
独立做过软硬件结合的项目
做过硬件相关的产品并找好供应链量产

## Slide 11: Outline
PPT部分
了解NFC和PCB
如何设计一款NFC卡片
操作部分
从设计到交付的全流程
学会读懂Datasheet并按照厂商的标准来设计
PCB设计软件的使用
Datasheet阅读
原理图设计
元件选型和采购，封装确认
绘制天线
PCB Layout设计
交付打样的流程

## Slide 12: NFC
Near-field communication

## Slide 13
NFC Tags and chips
The two components, the NFC chip and antenna, work together to form a self-contained functional device.

## Slide 22: Video
NFC Technology - STMicroelectronics.mp4

## Slide 23: Basic antenna theory for NTAG I2C plus tags
6

## Slide 24: NTAG I2C plus electrical input capacitance
7
NTAG I2C plus IC
FD
Vout
SCL
SDA
Gnd VCC
to MCU
NTAG I2C plus equivalent circuit
CIC= NTAG I2C plus input capacitance (50pF)
La
Lb
NTAG I2C plus IC connections
La, Lb = NTAG I2C plus pads to be connected to the antenna
It is the most important factor for the
antenna design.
The form factor and the parameters of the antenna are affected by the input capacitance
NTAG I2C plus IC input capacitance
Antenna coil

## Slide 25: Antenna coil electrical equivalent circuit
8
NTAG I2C plus IC
FD
Vout SCL
SDA
Gnd VCC
to MCU
NTAG I2C plus equivalent circuit
CIC= NTAG I2C plus input capacitance (50pF)
La
Lb
Antenna coil
A
n t e
n
na
c o
i l
Antenna coil
Antenna coil equivalent circuit
Each antenna is a resonant circuit with a specific input impedance.
This input impedance is complex and consists of an inductance, capacitance as well as some losses represented by a resistance.
The actual values depend on
Antenna material
Thickness of conductor
Distance between the windings
Number of turns
Shielding layer
Environment

## Slide 27: Antenna design procedure for NTAG I2C plus tags
11

## Slide 28: Antenna design procedure for NTAG I2C plus tags
12
The precision of the antenna equivalent inductance computation, the length of the connection between the chip and its antenna, and the environment (metal surface, ferromagnetic material) impact the tuning frequency.
1. Design the antenna coil
Determine the size and the specs of the antenna
(number of turns, track width, spacing, etc.)
2. Measure antenna coil
Characterize R,L,C antenna coil parameters
3. Calculate the resonant capacitor value Determine the value of resonant capacitor to set the tag to the target resonant frequency
4. Assemble & measure resonant frequency Measure the resonant frequency and adjust the capacitor value if needed
Antenna coil
NTAG I2C plus + antenna coil= resonance circuit
NTAG I2C plus |  | Connection / Assembly |  | Resonant capacitor |  | 

## Slide 29: Design the antenna coil
13

## Slide 30: Antenna class based on ISO/IEC14443
14
ISO/IEC 14443-1 defines 6 antenna classes, also referred to in ISO/IEC 15693.
The use of ISO/IEC14443 antenna class is optional but it has been established that the use of a prescribed class may enhance interoperability

## Slide 31: Antenna parameters for rectangular and round antennas
15
Inductance of an antenna depends on the antenna dimensions and material properties
Antenna geometry
a0 → Definition of the overall length (mm)
b0 → Definition of the overall width (mm)
w → Track width in mm
g → Gap between tracks (mm)
t → Track thickness
N → Number of turns
Antenna geometry
D0 → | Definition of the antenna diameter (mm) | •
w → g → t → N → | Track width in mm, Gap between tracks (mm), Track thickness Number of turns | •
Material properties
ρ → Electric conductivity εr → Permittivity of card material

## Slide 32: Coil design calculation sheet
Excel calculation sheet tool included in https://www.nxp.com/docs/en/application-note/AN11276.zip
16
This coil design guide calculation sheet uses antenna dimensions and estimates the antenna equivalent inductance.
The following steps are a reliable method to design and fine tune a custom antenna coil:
  Estimation of the electrical parameters
  Definition of the target inductance
  Definition of the dimensions
  Definition of the matrix run
  Production of samples
  Selection of the best coil parameters
  Definition of second matrix run (if needed)

## Slide 33: Measure the antenna coil parameters
17

## Slide 34: Measuring the antenna coil parameters
18
The antenna loop has to be connected to a network analyzer to measure the antenna equivalent circuit (Ra, La, Ca)
Before each measurement, the network analyzer must
be calibrated (open, short and load compensation).
  Settings: S11
  Chart: Smith Z
  Start frequency: 1 MHz
  Stop frequency: Above self-resonant frequency
Note: The antenna has to be at the final mounting position to consider all parasitic effects like metal influence on quality factor, inductance and additional capacitance
High-end or Low-end network analyzer (e.g., miniVNA PRO)
Fig. Antenna series equivalent circuit (Ca, La, Ra)
NTAG I2C plus
Antenna coil

## Slide 35: Calculate the resonant capacitor value
19

## Slide 36: Calculating the parallel resonance capacitor
20
NTAG I2C plus IC
A
n t e
n
na
c o
i l
Antenna coil
Rcon Ccon
Rcon
Connection
La
Lb
Antenna coil
𝐶
𝑓𝑟 − 𝑐𝑢𝑟𝑟𝑒𝑛𝑡
=
1
2 · 𝜋 · 𝑓
𝑟𝑒𝑠
2 · 𝐿
We measure the current system resonance frequency (𝑓𝑟 − 𝑐𝑢𝑟𝑟𝑒𝑛𝑡) after connecting the NTAG I2C plus to the antenna coil.
If it is not 𝑓𝑟 − 𝑐𝑢𝑟𝑟𝑒𝑛𝑡~ 13.56𝑀𝐻𝑧 , we calculate the system capacitance at the current resonance frequency with this formula:
Note: The inductance of the system is basically the inductance of the antenna (L=La).

## Slide 37
21
Calculating the parallel resonance capacitor (II)
If we fix the desired system resonance frequency (𝑓𝑟 − 𝑡𝑎𝑟𝑔𝑒𝑡), the capacitance required so that the system resonates at that target frequency can be calculated with this formula:
NTAG I2C plus IC
A
n t e
n
na
c o
i l
Antenna coil
Rcon Ccon
Rcon
Connection
La
Lb
Tag
CRes
Resonance capacitor
𝑡𝑎𝑟𝑔𝑒𝑡
𝐶 =
1
2 · 𝜋 · 𝑓𝑟
−
2 · 𝐿
𝑡𝑎𝑟𝑔𝑒𝑡
We can calculate the extra capacitance that needs to be soldered in parallel (CRes) by:
𝐶𝑅𝑒𝑠 = 𝐶𝑡𝑎𝑟𝑔𝑒𝑡 − 𝐶𝑓𝑟 − 𝑐𝑢𝑟𝑟𝑒𝑛𝑡
Note: For single tag operation, a tuning slightly above 13.56 MHz would lead to maximum read-/write distance. Due to manufacturing tolerances, a nominal frequency of 14.5 MHz for single tag operation is recommended.
Antenna coil
Resonance capacitor

## Slide 38: Assemble & measure resonant frequency
22

## Slide 39: Assembling and measuring the tag resonant frequency
23
Assemble the calculated 𝑪𝒓𝒆𝒔 capacitor in your design.
Then, measure the resonant frequency (𝒇𝒓𝒆𝒔) at which the resistance impedance (Z) is maximum
If the resonant frequency is not the target resonant frequency, fine tune the capacitor value. If the frequency is high, increase the capacitor value; if low, decrease it.
Resonance Antenna coil
capacitor
Fig. Example of a tag adjusted to 𝒇𝒓𝒆𝒔 = 13.564 MHz

## Slide 40: Design
How to design a good-looking and stable NFC Tag PCB

## Slide 41: ISO 7810
ISO 7810，是身份证、银行卡等尺寸的国际标准，分为ID-1、ID-2、ID-3及ID-000四种。现时采纳的版本为2003年版。
样式 | 尺寸 | 用途
ID-1 | 85.60 × 53.98 mm | 绝大多数银行卡及身份证
ID-2 | 105 × 74 mm | 法国身份证等；签证
ID-3 | 125 × 88 mm | 护照
ID-000 | 25 × 15 mm | SIM卡
ID-1的规定尺寸为85.60×53.98毫米（3.370×2.125英寸），常用于身份证、银行卡（如提款卡、信用卡）、驾照、个人名片，以及商店发出的忠实顾客卡等。
其长宽比与黄金分割（1.618:1）接近。
ISO 7813规范ID-1塑胶银行卡的附加特性，包括0.76毫米厚度，及3.18毫米半径的圆角。

## Slide 42
设计为
85.60×53.98毫米
3.18毫米半径的圆角
0.76毫米厚度（做0.8mmPCB板）

## Slide 43: 丝印和Top图案设计和导入
使用Ai设计表面丝印BMP

## Slide 47: PCB Intro
What is PCB

## Slide 48
PCB的材料和结构
材料—玻璃纤维
结构—多层板
铜膜（敷铜板）
玻璃纤维板
Top Layer (元件面)
Bottom Layer (焊接面)
插针式元件
SMD元件
焊锡
Via (过孔)
Notes: 两种：
通孔式：
表面式：

## Slide 49: Video
https://www.bilibili.com/video/BV1pf4y1v7RL/

## Slide 50: PCB Design Software
Altium Designer
KiCAD
Autodesk Eagle
…… etc.

## Slide 51: PCB代工厂
嘉立创
国外：https://jlcpcb.com/
国内：https://www.sz-jlc.com/
捷多邦
国外：https://www.pcbway.com/
国内：https://www.jdbpcb.com/

## Slide 52: KiCad EDA
A Cross Platform and Open Source Electronics Design Automation Suite

## Slide 53
Introduction to KiCad
KiCad is an open-source software tool for the creation of electronic schematic diagrams and PCB artwork. Beneath its singular surface, KiCad incorporates an elegant ensemble of the following stand-alone software tools:
Program name | Description | File extension
KiCad | Project manager | *.pro
Eeschema | Schematic and component editor | *.sch, *.lib, *.net
Pcbnew | Circuit board and footprint editor | *.kicad_pcb, *.kicad_mod
GerbView | Gerber and drill file viewer | \*.g\*, *.drl, etc.
Bitmap2Component | Convert bitmap images to components or footprints | *.lib, *.kicad_mod, *.kicad_wks
PCB Calculator | Calculator for components, track width, electrical spacing, color codes, and more…​ | None
Pl Editor | Page layout editor | *.kicad_wks

## Slide 57: Thanks
My Wechat ID lbyzztl